## Slide 1: SunGuide Operator Training
Release 8.0
2020

## Slide 2: Agenda
Part 1: Introduction
  SunGuide Operator Training
  SunGuide Overview
  Operator Map
Part 2: Traveler Messages
  Dynamic Message Signs (DMS)
  Highway Advisory Radio (HAR)
  Beacons
Part 3: Cameras and Video
  Closed Circuit Television (CCTV)
  Scheduled Actions Subsystem (SAS)
  Video Switching and Control
Part 4: Roadway Monitoring
  Roadway Weather Information Systems (RWIS)
  Transportation Sensor Subsystem (TSS)
  Connected Vehicle (CVS)
  AVI / LPR Traffic Sensors
  Travel Times (TvT)
  Safety Barrier (SB)
  Center-to-Center (C2C) Devices
  General Purpose Input/Output (GPIO)
Part 5: Event Management (EM)
  Events and Event Details
  Response Plan Generation (RPG)
  Rapid Incident Scene Clearance (RISC)
  Event Management Auditing
  Incident Detection Subsystem (IDS)
  511 Floodgates
  Road Ranger Management
  Smart Phone Application for Road Rangers (SPARR)
Part 6: Reporting
  Reporting Subsystem
  Regional Integrated Transportation Information System (RITIS)
Part 7: Additional Traffic Management
  Managed Lanes
  Traffic Control
  Truck Parking
  Ramp Metering

## Slide 3: Part 1: Introduction

## Slide 4: SunGuide Operator Training

## Slide 5: Purpose of Operator Training
Initial exposure to SunGuide software, concepts, and latest changes/enhancements
Training should continue in “live” operational environment
Explains how to use the software
  Operational procedures differ from district to district
  Operators should follow district-specific procedures

## Slide 6: Training Format
Step through concepts and windows on a section by section basis
After each section, operators will have “hands on” time to familiarize current portion of the software
Feel free to ask questions any time
  Deviating from the course material is welcomed

## Slide 7: House Keeping
Please sign in and PRINT clearly
Breaks built into training

## Slide 8: SunGuide Overview

## Slide 9: SunGuide Architecture
SunGuide Software
FDOT District X
Devices
(DMS, CCTV, AVL, AVI, etc…)
RTMC Operators
SunGuide
Database
SunGuide C2C
Road Ranger Tablet/ SPARR
SunGuide C2C
FDOT District Y
SunGuide
DB
SunGuide C2C
FDOT District Z
SunGuide
DB
C2C
FL ATIS (511)
511
Website
FL ATIS
3rd Party Traffic Data
(NOKIA, HERE, BlueTOAD, etc.)

## Slide 10: SunGuide Software Architecture

## Slide 11: Operator Map

## Slide 12: Logging In
Username and Password
  Both are Case Sensitive
  Administrator creates/edits user accounts (via the Admin Editor)
Subsystem Loading Progress Displayed
Watch System Messages for Extra Information

## Slide 13: SunGuide Subsystems
Gray = User is not connected
Red Slash = subsystem is offline (often an error condition)
Colored “Ready” = user connected and subsystem is online
  Checkboxes to selectively login

## Slide 14: Map: Managing Your View
Zooming:
  Zoom buttons in Navigation Panel
Panning:
  Click and drag map
Jump to Views:
  Cities
  Districts
  Areas of Interest
  Drop down box in panel
Zooming

## Slide 15: Map: General Concepts
Main Context Menu
  Right click on background of map
Common functionality for each subsystem
Device Status
  Active: Operating normally
  Error: Communication or other problem, will be polled normally
  Failed: Several consecutive errors, will no longer be polled normally
  Out of Service: Manually disabled
  Device icons typically colored based on status
Device / Event Icons
  Left click: Status
  Right click: Context menu for item

## Slide 16: Map: Preferences
Preferences Menu
  Save Current Map View
    Re-centers zoomable area of map
  Save Current Window Positions
    Windows will reopen to current position
    General windows will reopen on login
  Subsystems
    Opens the window listing the subsystems that the user is logged into
  Tile Sets
    Allows user to change the “tiles” used to draw the map

## Slide 17: Map: Icon Configuration
Icon Configuration is found at the top left corner of the map
Selected icons are displayed on the map
The color of icon states can be altered
Displayed on map if checked

## Slide 18: Map: System Messages
Notifies users of errors / warnings from various subsystems
Can selectively receive different types of messages

## Slide 19: System Settings
Configuration

## Slide 20: Map View Configuration
Zoom and pan to specific areas of the map
Save map view
Views are accessible from all users

## Slide 21: System Configuration
Category-based configuration settings
Globally defined

## Slide 22: Map Shield Editor
Create and place shields on map

## Slide 23: Queue Settings
Under the Queue Settings Configuration, an administrator can define the maximum number of phases for both manually posted messages as well as messages that are auto-configured.
MUTCD status this should be set to a maximum of 2 phases.
Notes: Response plans will be discussed in detail in the next section

## Slide 24: User Configuration
Manage SunGuide user accounts
  Individual permissions
  Group permissions

## Slide 25: User Group Configuration
Users inherit group permissions

## Slide 26: Manufactures
List of manufactures
  Used for device management

## Slide 27: Display Coordinates
Devices can be configured for their physical location in the device specific dialog, and moved to a different location for easier use by operations

## Slide 28: Operator Map
Hands on
15 Minutes

## Slide 29: Part 2: Traveler Messages

## Slide 30: Dynamic Message Signs (DMS)

## Slide 31: DMS: Menu Options
DMS Device Context Menu (right-click on local DMS device)
DMS Context Menu (right-click on Operator Map)
Notes: Note that “Remote” DMS refers to other districts’ DMS. May not be applicable if C2C not configured for this.
Demo: DMS Menu:
Show the menu options for DMS

## Slide 32: DMS: Short Status
DMS Short Status Window
  DMS Device Context Menu
    Short Status
  Includes…
    Name
    Number of Messages in Queue
    Operational Status
    Few buttons for control

## Slide 33: DMS: Device List
Device list displays important information in tabular form in-line with device names
Rows can be sorted and filtered by column
Actions can be performed on multiple items by using Shift or Ctrl to select multiple DMSs

## Slide 34: DMS: Full Status
Full status
  From DMS Device Context Menu
  Or, from DMS Context Menu
  Or, from DMS Status Window and select “Detailed Status”
Full status is displayed in the “Status” tab
Notes: Need subject and verb (missing verb) hard to tell what is being presented from bullets

## Slide 35: DMS: Message Queue
Message Queue
  Select “View Queue” from the Short Status
  Or, Select a DMS device from the Device Messaging Window and click on the “Queue” tab
Shows list of messages currently queued

## Slide 36: DMS: Send Message
Send message
  From Short Status Window
  Or, from “Add Message” button within the Device Messaging Window
Ability to create messages with:
  Multiple pages
  Graphics
  Inline Graphics
  Alignment
  Custom Colors
Notes: Maybe point to controls for the list of items

## Slide 37: DMS: Send Message (Font)
Based on the configuration, Fonts can also be changed as you send a message
Notes: Maybe point to controls for the list of items

## Slide 38: DMS: Send Message (Alignment)
The DMS dialog allows a user with permission to change the alignment of the text on the line.
The alignment tag can be seen in the textbox where the user types and would apply to the rest of the message of until another alignment tag is encountered.
Notes: Response plans will be discussed in detail in the next section

## Slide 39: DMS: Send Message (Full Graphic with Alignment)
Alignment of a full size graphic can be set as well
Alignment will only apply to the full size graphic and not the text
Notes: Response plans will be discussed in detail in the next section

## Slide 40: DMS: Send Message (Inline Graphics)
Users can add inline graphics that are the size of a single line or smaller
Inline graphics follow the alignment of the line they are placed on
Notes: Response plans will be discussed in detail in the next section

## Slide 41: DMS: Message & Graphic Library Management
Manage Libraries from the Operator Map DMS Context Menu
  Graphic Management
  Message Libraries
Add/Modify/Delete items

## Slide 42: DMS: Device Messaging Window Menus
Use the top menu within Device Messaging Window to control DMS Devices
DMS Devices can also be controlled by right-clicking the device within the Device messaging Window to bring up a Device-specific menu
  Select multiple DMS with Shift or Ctrl

## Slide 43: DMS: Device Messaging Window: Set Op Status
Set a DMS device’s operational status to:
  Active
  Out of Service
Select the device within the Device Messaging Window
Set the Status by:
  Click the “Set Op Status” button from the top menu
  Or, by navigate to “Set Op Status” within the Device-Specific menu

## Slide 44: DMS: Device Messaging Window: Refresh Status & Find on Map
Find on Map
  Select to circle device on Operator Map
  This option can only be found in the Device-Specific Menu
Refresh Status
  Refresh a DMS device’s status by selecting “Refresh Status”

## Slide 45: DMS: Device Messaging Window: Queue
Add Message
  Causes the Send Message Window to pop-up
  New message will be added to queue
Resend Top Message
  Sends the top message in the queue to the device
Blank Queue
  Removes all of the messages from the queue
  Removes the currently displaying message from the device

## Slide 46: DMS: Device Messaging Window: Queue
Message queue lists all messages sent from SunGuide to a DMS in priority order
  1 = highest priority, 255 = lowest priority
  Note: “Completed” queue state for successfully sent messages

## Slide 47: DMS: Device Messaging Window: Queue Messaging
Modify
  Brings up Edit DMS Message Window
  Very similar to Send Message
Merge
  Select multiple messages in Queue and click “Merge” to group messages
Unmerge
  Disassociates grouped messages
Remove
  Deletes selected message from Queue

## Slide 48: DMS: Device Messaging Window: Detailed Status
Retrieves Status of various DMS components
To select a component to view:
  Click the Detailed Status Button
  Or, Select Detailed Status from the Device-Specific menu
View the returned status of the chosen component(s) in the “Detailed Status” tab

## Slide 49: DMS: Device Messaging Window: Set Brightness
Set the Brightness for a DMS Device
Options for brightness level are:
  Auto, Day, and Night
To select the desired brightness for a DMS device
  Click the Set Brightness Button
  Or, Select Set Brightness from the Device-Specific menu

## Slide 50: DMS: Device Messaging Window: Set Control Mode
Set the Control Mode for a DMS device to:
  Central
  Central Override
To set the Control Mode for a DMS device
  Click the Set Control Mode Button
  Or, Select Set Control Mode from the Device-Specific menu

## Slide 51: DMS: Device Messaging Window: Other Controls
To view the Other Controls options for a DMS device
  Click the Other Controls Button
  Or, Select Other Controls from the Device-Specific menu
After selecting an option from the menu, the bottom bar will post a notification concerning the success of the operation
  A dropdown will show more notices

## Slide 52: Dynamic Message Signs (DMS)
Configuration

## Slide 53: DMS: Configuration Sign Configuration
Lists all DMS, attributes, and connection info
  Sort upon column click
  Click “Save” after adding and/or editing one or more
Confirm successful save with Green Check

## Slide 54: DMS: Configuration Sign Configuration
Signs can also be auto-configured if NTCIP
Once the user enters the connection information, the user is able the query the sign to set the DMS values that can be retrieved from the sign
Notes: Response plans will be discussed in detail in the next section

## Slide 55: DMS: Configuration Sign Configuration
The default Font and values from the sign can be retrieved and reviewed.
Signs should be “Verified” so the system knows what values for the DMS should be used.
Notes: Response plans will be discussed in detail in the next section

## Slide 56: DMS: Configuration
Additional Fonts can be retrieved from the sign and configured in the system
Notes: Response plans will be discussed in detail in the next section

## Slide 57: DMS: Configuration Approved Words
Lists words alphabetically
  Case-insensitive

## Slide 58: DMS: Configuration Font Configuration
Specify font with height, spacing, and default width
  Optional characters with non-default widths

## Slide 59: DMS: Configuration DMS Group Editor
DMS grouping
  Used to filter DMS by groups

## Slide 60: DMS: Configuration DMS Manufactures
Listing of Sign Manufactures
  Listed in alphabetical order

## Slide 61: Highway Advisory Radio (HAR)

## Slide 62: How does HAR work?
SunGuide Operator
Text-to-Speech via the Radio
Text Event Report
SunGuide operator creates and sends selected HAR event information
  By selecting HAR
  By generating a Response Plan
Activated HAR translates text information to voice audio file and report over the radio
Drivers hear traffic report on the radio

## Slide 63: HAR: Context Menus
Main HAR Context Menu
Device Icon Context Menu

## Slide 64: HAR: Messaging
Uses the same Device Messaging window used for DMS
  Send HAR Message window differs
Notes: Similar to DMS status window.
- Lists all HAR stations in list in upper left hand corner
List of HAR can be filtered
Can activate/deactivate beacons
Stop message
Click “Send Message” to send new message or override the current message

## Slide 65: HAR
Configuration

## Slide 66: HAR: Configuration
HAR driver and configuration details for each HAR site
Notes: Similar to DMS status window.
- Lists all HAR stations in list in upper left hand corner
List of HAR can be filtered
Can activate/deactivate beacons
Stop message
Click “Send Message” to send new message or override the current message

## Slide 67: Beacons

## Slide 68: Beacons

## Slide 69: Beacons
Configuration

## Slide 70: Beacons: Configuration
Specify sign type, connectivity, and location

## Slide 71: DMS and HAR
Hands on
20 Minutes

## Slide 72: Part 3: Cameras and Video

## Slide 73: Closed Circuit Television (CCTV)

## Slide 74: CCTV: Camera Control
Control Camera
  Pan
  Tilt
  Nudge
  Zoom
  Focus
  Iris
Lock:
  Release
  Override
Presets:
  Save
  Recall
Selected Camera May Be Controlled By USB Joystick
Notes: Local refers to cameras that are integrated with the local TMC’s SunGuide system
Locking refers to the system only allowing one user, either a person or process, to control the camera at a time. Typically, this is an automatic feature whereby a lock is acquired or overridden automatically whenever a PTZ command is issued by any operator or by the joystick; however, advanced configurations can be setup that restrict the override and thus the release lock feature is necessary for other users without the override permission to acquire the lock (without having to override it from another user)
If camera is locked by moving a camera (i.e. issuing a PTZ command), the camera will automatically unlock if the camera is not moved for a configurable amount of time. Manually locking by clicking “Lock” will lock the camera permanently until unlocked.
Cameras list (upper left hand corner of window) will allow operators to select different cameras.
Demo: CCTV Camera Control
Show the ptz, nudge, presets, and locking features
Save a preset and jump to the preset

## Slide 75: CCTV: Advanced Camera Functions
Camera Menus
  Select display time
  Up, Down, Left, Right buttons navigate
  Enter to select
  Some cameras use page and value buttons, some do not
Detailed Data
  Select data type
  Select additional parameters, if necessary
  Press Get Details
  Response will be displayed in a new window
Notes: These features are not normally used as the standard camera control dialog is adequate

## Slide 76: CCTV: Video on Desktop (VoD)
Integrated into Operator map
  Double-click, drag-and-drop
Full-featured and detailed for usability
  User saves/loads VWW viewer positions (and tours)
  PTZ control and preset buttons in viewer
  Full screen
    Virtual video wall in monitor
    Viewer in the virtual video wall
  Support for video tour “drag and drop-on-top”
    Tour configuration saved with virtual video wall layout

## Slide 77: VoD: Menus
Main Video on Desktop (VoD) Menu
Camera Specific Context Menu

## Slide 78: VoD: Definitions
Window can contain any number of viewers
Viewer can contain any number of camera streams /tours
Window
Viewers

## Slide 79: VoD: Window and Viewer Creation
Windows are created through:
  Operator map context menus
  Top level VoD menu
Viewers can be created through:
  Operator map context menus
  Drag and drop of icons from OM
  Top level VoD menu

## Slide 80: VoD: Viewer Manipulation
The position and size of viewers can be altered in the following ways:
  Resizing the window
  Drag and drop of viewers
  Or, Right-click on camera icon
    Select the Desktop Video Wall from the “Desktop Video Dialogs” submenu

## Slide 81: VoD: Tour Creation and Editing
Dynamic tours can be created by dragging camera streams into the center of an existing tour or camera stream
Saved tours can be created through the VoD menu or by saving a dynamic tour.

## Slide 82: VoD: Camera Controls
Pan/Tilt
Lock Camera
Zoom
Focus
Presets
Right click
Notes: Video switching places a selected CCTV into a display
In tours, a single display cycles through multiple CCTV cameras. Allows operators cycle through multiple cameras on one display.
Demo: Switching Video
Switch an encoder to a decoder
Configure a tour and switch the tour to a decoder

## Slide 83: VoD: Camera Controls
Expand List of Cameras
Drag and Drop Cameras from List

## Slide 84: VoD: Window Menu Options
New
  Open a new Desktop View Wall window or video panel
Options
  Hide/Show Labels
  Stretch/Unstretch Video
  Play/Stop Video
Layouts
  Save/Load/Delete video layout
Tours
  Save/Delete/Use Video Tours
  Also, right-click on video to select/edit tour

## Slide 85
Click “Camera Blocking” from Cameras context menu
Page lists all cameras posting images to the public website
Images not appropriate for public consumption should be blocked
Click “Block” to block the image from the 511 (FL ATIS) website
CCTV: Camera Blocking
Notes: This does not affect the local SunGuide system and local video viewing capabilities. Image blocking is only for external systems. In the current design, this only blocks camera images from the FL ATIS website.
Demo: CCTV blocking
Show the CCTV Tabbed GUI and block video from FL-ATIS

## Slide 86
Set reminders for blocked cameras
CCTV: Camera Blocking
Notes: This does not affect the local SunGuide system and local video viewing capabilities. Image blocking is only for external systems. In the current design, this only blocks camera images from the FL ATIS website.
Demo: CCTV blocking
Show the CCTV Tabbed GUI and block video from FL-ATIS

## Slide 87: Keyboard / USB Joystick
Joystick can be used for simple PTZ
Manual Control Panel (MCP)
Capabilities
  Control CCTV devices (pan, tilt, zoom, focus, iris)
  Switch video (monitors or video wall)
  Display tours
Device Naming
  Numeric prefix required for cameras, monitors, and video wall viewers (example: 101-CCTV1)
Notes: Demo Prep: SunGuide system with video streams and decoders that are viewable and a configured AD keyboard
Demo: Demonstrate the various functions as presented on the slides

## Slide 88: Closed Circuit Television (CCTV)
Configuration

## Slide 89
Configure PTZ connection control
  Configuration must match camera controller configuration
  If polling set to ZERO, camera will not poll. Will not get iris, focus, and wiper settings
  One or more video streams per camera
CCTV: Camera Configuration
Notes: This does not affect the local SunGuide system and local video viewing capabilities. Image blocking is only for external systems. In the current design, this only blocks camera images from the FL ATIS website.
Demo: CCTV blocking
Show the CCTV Tabbed GUI and block video from FL-ATIS

## Slide 90
Define buttons on USB Joystick
CCTV: Camera Configuration
Notes: This does not affect the local SunGuide system and local video viewing capabilities. Image blocking is only for external systems. In the current design, this only blocks camera images from the FL ATIS website.
Demo: CCTV blocking
Show the CCTV Tabbed GUI and block video from FL-ATIS

## Slide 91: Scheduled Actions Subsystem (SAS)

## Slide 92: SAS: Definitions
What is a sequence?
  A series of CCTV positions / zoom levels / presets
  Example: A sequence is configured to have Preset 1 and Preset 3 only. Activating that sequence would make a camera go to Preset 1, then Preset 3, then Preset 1, then Preset 3, etc…
What is a schedule?
  When activated, it starts and stops a sequence for a configured camera/cameras at a specified times
A sequence defines the actions to take while a schedule defines the times the sequence is activated

## Slide 93: Accessing the SAS GUI
From the operator map menu, select “Scheduled Actions…” to bring up the SAS GUI

## Slide 94: SAS GUI Menus
SAS Main Menu: Located at the top of the GUI
Schedule-Specific Menu
  Right-click on a Schedule within the Schedule box, or within the box itself

## Slide 95: Add a New Schedule
There are two ways to add a new schedule
  Click the “Add New Schedule” button located in the SAS Main Menu
  Select “Add New Schedule” from the Schedule-Specific Menu

## Slide 96: Add a New Schedule, cont’d
Once the option to add a new schedule has been selected, a new schedule will appear in the “Schedules” box within the SAS GUI
The new schedule can be renamed by single-clicking the name of the schedule, tying the new name, and pressing Enter.

## Slide 97: Add a New Item to a Schedule
Highlight the desired schedule within the “Schedules” box by clicking on the schedule.
To Add New Item
  Click the “Add New Item…” button in the main menu
  Or, select “Add New Item to Schedule” from the Schedule-Specific menu

## Slide 98: Add New Item: Scheduling
Within the “Add Scheduled Items” window
  Name of the Item may be changed
Within the “Scheduling” Tab
  Time/length of the event
  Recurrence pattern and frequency
  Ability to archive (Deprecate) the schedule item when complete.

## Slide 99: Add New Item: Devices
Specify devices to be used for an action
  Select action type
Once Action Type selected, window will be populated with associated devices
  Use checkboxes to select devices

## Slide 100: Add New Item: Actions
After selecting devices, specify action to be taken
  Select “Actions Tab”
Select Action
  For schedule “devices” , Activate or Terminate
  For any TvT “devices”, Enable or Disable Travel Times
CCTV and DMS have more complex action options

## Slide 101: Add New Item: CCTV Actions
For CCTV devices, the user specifies an action list
  Actions include speed, duration, and action type
Custom action list or saved action list
  Available saved lists are selected from a drop down

## Slide 102: Add New Item: DMS Actions
For DMS devices, the user specifies a message to be displayed
  Select a predefined message from the library on the left
  Or, specify a custom message on the right

## Slide 103: Add New Item: Report Actions
For reports, the user specifies the following:
  Which report to run
  Output document format
  Whether or not to send the report to one or more emails
  Dynamic date range
  Report parameters

## Slide 104: Add New Item: Response Plan Actions
For response plans, the user chooses an event on the items tab.
The action choices are to activate or deactivate the response plan for the chosen event.

## Slide 105: Add New Item: Predefined Plan DMS Activation
Predefined Plans can be activated through SAS
Only DMS messages are sent, regardless of other pre-defined plan items
Allows messaging to Color/Non-Color DMS with different messaging, graphics, and colors
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 106: Add New Item: Change Permission Group Membership
SAS allows administrators to control permissions groups
Users can be selected to add/remove from a group in SAA.
Notes: Response plans will be discussed in detail in the next section

## Slide 107: Modify an Existing Item
To Modify, right-click item on the calendar,
From Event-Specific Menu
  Modify
  Delete
  Disable
“Edit Scheduled Item” opens the Edit Scheduled Item window, which is identical to the “Add Scheduled Item” window.

## Slide 108: Activate/Terminate Schedule
To Activate
  Click “Activate Schedule” from the Main Menu
  Or, Right-click desired schedule and select “Activate Schedule” from the Schedule-Specific Menu
To Terminate
  Right-click the desired active schedule and click “Terminate Schedule” from the Schedule-Specific Menu
  Or, Select an active schedule and click “Terminate Schedule” from the Main Menu

## Slide 109: Duplicate/Delete Schedule
Within the Schedule-Specific Menu
  Duplicate Schedule
  Delete Schedule
Duplicating a schedule will create a full copy of the selected schedule
Deleting a schedule, will remove the schedule and all of the items within it

## Slide 110: Scheduled Actions Calendar
The mini calendar can be used for navigation
Customize the schedules in the calendar by selecting the desired schedules using the checkboxes
Change the visible date range using the options in the Main Menu:
  Day
  Week
  Month

## Slide 111: Calendar: Day View

## Slide 112: Calendar: Week View

## Slide 113: Calendar: Month View

## Slide 114: Edit Saved Action Lists
To view/create/modify/delete action lists, select the “Edit Saved Action Lists” button located in the Main Menu
Select selected Action List
  Or, click “Add List”
Select action to:
  Add
  Delete
  Modify
  Reorder

## Slide 115: Reactivate Schedule Item
Archived scheduled items can be retrieved and re-added to the system by clicking the Search Scheduled Items ribbon button.
Select the time period or type of item to retrieve and a list of matching items will be displayed to the user.
Notes: Response plans will be discussed in detail in the next section

## Slide 116: Video Switching and Video Wall Control

## Slide 117: Video Switching
Video sources and tours can be drag and dropped onto selected virtual wall
Notes: Video switching places a selected CCTV into a display
In tours, a single display cycles through multiple CCTV cameras. Allows operators cycle through multiple cameras on one display.
Demo: Switching Video
Switch an encoder to a decoder
Configure a tour and switch the tour to a decoder

## Slide 118: Video Wall
Video sources and tours can be drag and dropped onto selected video wall
Notes: Video switching places a selected CCTV into a display
In tours, a single display cycles through multiple CCTV cameras. Allows operators cycle through multiple cameras on one display.
Demo: Switching Video
Switch an encoder to a decoder
Configure a tour and switch the tour to a decoder

## Slide 119: Video Switching
Configuration

## Slide 120: Video Switching
Create and design virtual video walls
Configure video destination layouts
Notes: Video switching places a selected CCTV into a display
In tours, a single display cycles through multiple CCTV cameras. Allows operators cycle through multiple cameras on one display.
Demo: Switching Video
Switch an encoder to a decoder
Configure a tour and switch the tour to a decoder

## Slide 121: Video Switching
Video destinations configured and connect individually
Notes: Video switching places a selected CCTV into a display
In tours, a single display cycles through multiple CCTV cameras. Allows operators cycle through multiple cameras on one display.
Demo: Switching Video
Switch an encoder to a decoder
Configure a tour and switch the tour to a decoder

## Slide 122: Video Switching
Configure workstations to manage video destinations
Notes: Video switching places a selected CCTV into a display
In tours, a single display cycles through multiple CCTV cameras. Allows operators cycle through multiple cameras on one display.
Demo: Switching Video
Switch an encoder to a decoder
Configure a tour and switch the tour to a decoder

## Slide 123: Video Switching
Video sources configured and connect individually
Notes: Video switching places a selected CCTV into a display
In tours, a single display cycles through multiple CCTV cameras. Allows operators cycle through multiple cameras on one display.
Demo: Switching Video
Switch an encoder to a decoder
Configure a tour and switch the tour to a decoder

## Slide 124: Video Switching
Tours
  Allows operators to cycle through cameras, but does not move camera positions
  Set dwell time to display each source
Notes: Video switching places a selected CCTV into a display
In tours, a single display cycles through multiple CCTV cameras. Allows operators cycle through multiple cameras on one display.
Demo: Switching Video
Switch an encoder to a decoder
Configure a tour and switch the tour to a decoder

## Slide 125: CCTV, SAS, and Video Switching
Hands on
45 Minutes

## Slide 126: Part 4: Roadway Monitoring

## Slide 127: Roadway Weather Information System (RWIS)

## Slide 128: RWIS: Status
View Status and reported measurements per RWIS
RWIS alarms will appear in alerting window
Notes: Displays all data reported from each RWIS site.
A site likely does not report all reportable data. For example, if a site only reports temperature and wind speed, all other fields in SunGuide will report “no data”.
Window has white tabs at the top which allows operators to select different categories of weather data
Stations list (upper left hand corner) allows the selection of any site

## Slide 129: Roadway Weather Information System (RWIS)
Configuration

## Slide 130: RWIS: Configuration
Add / Delete Stations
Notes: Displays all data reported from each RWIS site.
A site likely does not report all reportable data. For example, if a site only reports temperature and wind speed, all other fields in SunGuide will report “no data”.
Window has white tabs at the top which allows operators to select different categories of weather data
Stations list (upper left hand corner) allows the selection of any site

## Slide 131: RWIS: Configuration
Alarm and/or Activate Response Plans based on thresholds
Notes: Displays all data reported from each RWIS site.
A site likely does not report all reportable data. For example, if a site only reports temperature and wind speed, all other fields in SunGuide will report “no data”.
Window has white tabs at the top which allows operators to select different categories of weather data
Stations list (upper left hand corner) allows the selection of any site

## Slide 132: Transportation Sensor Subsystem (TSS)

## Slide 133: TSS: Overview
Detector Types
  RTMS: Remote Traffic Microwave Sensor
  MVDS: Microwave Vehicle Detection System
  Inductive Loops
  User Interface does not differentiate between detector types
Traffic Data
  Speed and occupancy data down to the “lane” level
  Generates “alarms” which indicate an abnormal traffic condition
Data Organization
  Lane: Individual detection zone (one point on freeway)
  Link: Collection of lanes across freeway
  Detector: Field unit which collects traffic data
Notes: There are two main categories of detectors: probe and point
Point detectors provide a sample of data on what is happening at one point on the roadway and is assumed to be representative of the roadway conditions some short distance before and after the sample
Probe detectors virtually insert a probe into the system and measure the time it takes for the probe to travel through the system. Travel times along links can then be calculated. The virtual probe actually are vehicles already in the system and the Probe detectors simply identify the same vehicle at a beginning and ending point to use as the virtual probe, noting the exact time the probe was present at each detection point. Typically, the license plate or the electronic toll tag is used/read as the identifier of the probe.
Occupancy is a measurement of the percentage of time in which a detector is occupied by a vehicle
Volume is the quantity of vehicles that pass a reference point per unit of time

## Slide 134: TSS: Context Menu
Main TSS Context Menu
Detector Icon Context Menu
Active Alarm Context Menu
Notes: Permissions show the related user permissions
Context menus shows the various ways to access the TSS component user interface dialogs
Demo: open a detector status and a link status dialog from the context menus and leave open for use in the next demo

## Slide 135: TSS: Detailed Data
Traffic Data for all links, select to view lanes
Notes: TSS has two different status windows.
TSS Link Data window:
Operator opens window by clicking on the speed-colored link (lanes), not the device icon
Reports speed, occupancy, and volume
Narrow pink bars are the last read received from the site
Blue bars are the “smoothed” data, an average speed/occupancy over x (usually about 5) minutes
TSS Detector Status
Operator opens window by clicking on the operational status-colored device icon
Reports device location and operational status
Demo: TSS Detailed Data
Show the link and detector status dialog
Change the operational status and watch the simulator report the disconnection and reconnection

## Slide 136: TSS: Nokia / HERE Data
What is Nokia / HERE?
  Third Party Vendor that FDOT has paid to provide travel speed data
  Data purchased includes travel speed data to FDOT for interstate and arterial roadways throughout Florida
  Available to all districts
Nokia
HERE
District 2
District 3
District N
FL-ATIS
Traveling Public
Notes: All Districts have the option to connect to the Nokia web service and acquire HERE speed data
HERE data can be combined into travel time links and provided to FL-ATIS

## Slide 137: TSS: BlueTOAD / Other External Sources
BlueTOAD (Bluetooth Travel-time Origination And Destination) detects anonymous MAC addresses through Bluetooth.
The system calculates travel time through analysis of subsequent detections.
Data received in SunGuide in a similar fashion to INRIX.

## Slide 138: Transportation Sensor Subsystem (TSS)
Configuration

## Slide 139: TSS: Configuration
Several steps to configuring TSS
  Configure and Calibrate detector (outside of SunGuide)
  Add detector to SunGuide
  Add one or more links associated with detector
  Add one or more lanes per link
  Add alarming thresholds group
    Each link can be added to only one group
  Add links to operator map

## Slide 140: TSS: Configuration
Step 1: Configure and Calibrate detector (outside of SunGuide)
  Likely require a combination of vendor software and site visit
  Ensure network routing and connection information is verified
  NOTE: Make sure detector is reporting all expected lanes. Lanes are configured manually into SunGuide. SunGuide will not automatically determine the number of reported lanes.

## Slide 141: TSS: Configuration
Step 2: Add detector to SunGuide

## Slide 142: TSS: Configuration
Step 3: Add one or more links associated with detector

## Slide 143: TSS: Configuration
Step 4: Add one or more lanes per link

## Slide 144: TSS: Configuration
Direction of Travel
Detector
Point-Speed Detectors
Lane #
1 2 3
2 1 0
Zone #
(if zero-based)
Direction of Travel
Downstream
Detector
Probe Detectors
Lane #
1 2 3
Zone #s depends on detectors
Upstream
Detector

## Slide 145: TSS: Configuration
  Step 5: Add alarming thresholds per link
    Create a TSS Threshold GROUP. Add link to the group. Link can only be added to a single group.
Notes: Response plans will be discussed in detail in the next section

## Slide 146
TSS Thresholds for speed and recovery are set on the GROUP
TSS: Configuration
Notes: Response plans will be discussed in detail in the next section

## Slide 147: TSS: Configuration
TSS Links are assigned to the group. Links can only be added to one group.
Notes: Response plans will be discussed in detail in the next section

## Slide 148: TSS: Configuration
  Step 6: Add links to operator map
    Requires careful drawing of links onto map to communicate to operators the location and geometry of roadway segments
    This configuration does not affect travel time calculates nor is it needed to archive reported data
    Adding of midpoints affects the network configuration reported from SunGuide via C2C

## Slide 149: TSS: Configuration
  Global TSS Configuration Settings

## Slide 150: Connected Vehicle Subsystem (CVS)

## Slide 151: CVS: What is Connected Vehicle?
Formally called “VII” and “Intellidrive”
Devices in vehicles provide information about the vehicle
  Speed
  Heading
  Location (latitude, longitude, elevation)
  Vehicle Size
  Brake Status
  Headlight Status
  Wiper Status
  More?
Road-side devices accepts this data and makes it available to SunGuide
For the initial release, only these are provided to SunGuide

## Slide 152: CVS: Getting Data to and from SunGuide
SunGuide
RSE
Road Side Equipment
RSEs are the collection points for connected vehicle data
Vehicle Data
TAMs
Traveler Advisory Messages
TAMs are rough equivalents to DMS messages

## Slide 153: CVS: Context Menu
Configuration Inspector
  Confirms if RSEs, Zones, TSS Links, and Lane Names have been configured without conflicts
RSE Configuration
  Allows adding, removing, and modifying RSE configuration
RSE Status
  Provides status and summarized data from RSEs
Traveler Advisories
  Allows adding, removing, and modifying TAMs

## Slide 154: CVS: RSE Configuration
Editor lists out all RSEs configured
Communication Tab
  ID must be unique and cannot exceed max length
    Max length depends on Zone name length
    SunGuide will notify user if length is exceeded
  IPs unique per site
  TAM ports depends on RSE configuration

## Slide 155: CVS: RSE Configuration
Location Tab
  Select available Roadways (from EM)
  Direction is NOT vehicle direction
    RSE position
    Does not affect vehicle data
  Lat/Lng in microdegrees
  No limits on description

## Slide 156: CVS: RSE Configuration
Detection Zones – Location Tab
  One zone required per vehicle direction of travel that is being read by RSE
    Recommend to use “NB”, “SB”, “EB”, and “WB” names to save space
  Heading is configured by using GUI’s range circle
    Yellow portion is heading range that a vehicle may be traveling; 0 Degrees is due North
  Length in approximate miles of roadway being detected
  # of Lanes of roadway being detected

## Slide 157: CVS: RSE Configuration
Detection Zones – Limits Tab
  If speeds drop below Alarm Threshold, a TSS alarm is triggered
  Alarm will clear if speeds exceed Recovery Threshold
  Speed Limit of roadway detected
  Is detected roadway an Arterial?
  Should vehicle data within zone be reported to FLATIS?

## Slide 158: CVS: RSE Configuration
Edit Zone Geometry
  Place points on map to outline area in which vehicles will be detected by RSE

## Slide 159: CVS: RSE Configuration
Must click “Save” after making additions, edits, and deletes
After Save, highlights will turn white and status will update

## Slide 160: CVS: RSE Configuration
TSS Links
  After the RSE is configured, the associated TSS Links need to be configured
  TSS Links will appear in the “Edit Link Placement” window per RSE per Zone
  Place nodes along roadway to match roadway geometry similar to other TSS Links

## Slide 161: CVS: RSE Status
Lists current status of configured RSEs
  Can change Op Status
Lists the current average speed and number of vehicles reporting speeds below or above alarm thresholds
Can filter list by Active, Error/Failed, Out of Service, with/without TAMs

## Slide 162: CVS: RSE Status
Find on Map
  Highlights RSE icon in Blue

## Slide 163: CVS: RSE Status
TSS Links
  Map displays RSE icon and one or more TSS Links
  TSS Links are direction-specific
  TSS Links should visually indicate the number of lanes detected
  Clicking TSS Link launches TSS Status window

## Slide 164: CVS: RSE Status
RSE Icons
  Rectangle at the bottom indicates the RSE device status (online, out-of-service, error, failed)
  Circle and Fan indicates if at least one TAM has been send to RSE
  Background indicates status of associated TSS

## Slide 165: CVS: TAM Status
Lists all TAMs currently being sent from SunGuide
Can filter list
Messages are always plain text
Priorities vary from 1 (highest) to 7 (lowest)
Event ID associated with TAM if created via Response Plan
# Regions are the geographic areas to which TAMs are broadcast
List of RSEs to which SunGuide is sending message

## Slide 166: CVS: Adding/Editing TAM
Type in TAM text
Set Priority
Set End Time
RSEs can be selected manually
  Or a Region can be created instead to automatically select RSEs

## Slide 167: CVS: Adding/Editing TAM
To create Region
  Click Add Region
  Select direction of travel of vehicles to receive TAMs
  Click Edit Geometry
  Add points to form area where TAM should be reported
  Click Done and then Save

## Slide 168: CVS: TAM via Response Plan
Generate a Response Plan
TAMs are listed as an output option
SunGuide will automatically generate TAM message and select RSEs based on event location
Active Response Plan to broadcast TAM

## Slide 169: Travel Times (TvT)

## Slide 170: Travel Times Status
Access the Travel Times Status page by clicking on “Travel Times…” from the context menu or clicking “Travel Times” from the green menu bar
Notes: TvT links are TSS links “added up”. These longer links are used to report common travel times between two points, such as from a DMS to a downstream exit or other destination.
Demo: Show Tabbed GUI’s TVT status Window

## Slide 171: Travel Times Status
Lists TvT Links, which may use a combination of loop detectors, AVIs, LPRs, etc
  TvT Link Name
  Calculated travel time
  Free flow travel time (based on speed limit)
  Delay (travel time minus free flow)
Notes: Link name describes the link, Current is the current calculated travel time, Freeflow is based off of the posted speed limit, and Delay is Current minus Freeflow.

## Slide 172: Travel Times Status
Click “Show” or “Hide” to view or hide DMS reporting the TvT link data
  Zero or more DMS may be reporting TvT link
  Green outline: message shown is currently displayed on DMS
  Violet outline: message shown is NOT currently displayed on DMS (a different message appears on the DMS, may imply DMS/comm failure)
Notes: Typically there is zero or one DMS associated with each TvT link.
DMS are highlighted green when the travel time message is actually posted on the DMS.
DMS are highlighted purple if the travel time message is not on the DMS, due to DMS/comms issues or because there’s a higher priority incident message on the DMS.
Demo: Show Travel Time Status DMS Message from Tabbed GUI

## Slide 173: Travel Times Status
Operator can enable/disable calculating travel times for any link by
  Selecting the checkbox on the Left column
  Clicking “Enable Links” or “Disable Links”
Highlight on Map will center the operator map and highlight in white the TSS links that comprise the TvT link
Notes: Demo: Show Enable Links, Disable Links, and Highlight on Map features of Tabbed GUI TVT Status

## Slide 174: Travel Times Status Alternate Routes
If only one TvT link is selected, operator can click “Alternate Routes” to open the Alternate Route Comparison window
  Lists routes that have the same start and same end but different paths
I-4 at SR 417 in Sanford
I-4 at SR 417 at Disney
SR 417 Route
I-4 Route
Notes: Demo: Show alternative routes of a TVT from Tabbed GUI TVT page

## Slide 175: Travel Times Status Matching Routes
If only one TvT link is selected, operator can click “Matching Routes” to open the Matching Route Comparison window
  Lists routes that have the same path but use different technologies to measure traffic
I-195 at DMS 105
I-195 at I-95
AVI TvT Link
Loop TvT Link
Notes: Demo: Show matching routes of a TVT from Tabbed GUI TVT page

## Slide 176: Travel Times (TvT)
Configuration

## Slide 177: Travel Time Configuration
Build TvT links with TSS links
Can combine TSS links using different technologies / sources
Can use portions of TSS links
Notes: Link name describes the link, Current is the current calculated travel time, Freeflow is based off of the posted speed limit, and Delay is Current minus Freeflow.

## Slide 178: Travel Times on DMS
Create a template for your DMS
Templates can used for any number of DMS
Templates could include color or monochrome
Notes: Link name describes the link, Current is the current calculated travel time, Freeflow is based off of the posted speed limit, and Delay is Current minus Freeflow.

## Slide 179: Travel Times on DMS
Associate a specific DMS to a template
Select one or more travel time destinations
Destination names configured separately
Notes: Link name describes the link, Current is the current calculated travel time, Freeflow is based off of the posted speed limit, and Delay is Current minus Freeflow.

## Slide 180: Travel Time Options
Global settings for generating travel times
Notes: Link name describes the link, Current is the current calculated travel time, Freeflow is based off of the posted speed limit, and Delay is Current minus Freeflow.

## Slide 181: Safety Barriers

## Slide 182: Safety Barriers: Overview
Monitors Vehicles Leaving Roadway
  Alarm is generated if vehicle breaks barrier at roadside
  Indicated on map by flashing SB icon
  Reset status / power / clock from window
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 183: Safety Barriers
Configuration

## Slide 184: Safety Barriers Configuration
Basic TCP/IP connectivity and location information
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 185: TSS, TvT, CVS, Safety Barriers
Hands on
30 Minutes

## Slide 186: Center-to-Center (C2C) Status and Control

## Slide 187: C2C Status and Control
What is Center-to-Center (C2C)?
  IIS-based software that operates outside of SunGuide
  Communicates device information and status
  Has limited device control capabilities
SunGuide 1
SunGuide 2
C2C Collector
C2C Provider
SunGuide 3
C2C Provider
C2C Extractor
C2C Extractor
C2C Provider
C2C Extractor
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 188: C2C Status and Control
C2C Context Menu
  Can select to view status and information received from C2C
SunGuide
C2C Extractor
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 189: C2C Select Networks
Select which incoming networks to view on the map
  C2C could provide multiple networks
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 190: C2C Camera Control
Camera Status and Control
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 191: C2C DMS Status
Similar Device Status Window as Local DMS
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 192: C2C Event List
Basic event information
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 193: C2C HAR Status
HAR Status and Control
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 194: C2C RWIS Status
RWIS Status and Control
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 195: C2C Traffic Conditions
View C2C TSS Links
Notes: Similar to HAR, Stations list allows operators to select any stations from list.
Indicates if/when alarm was triggered.

## Slide 196: General Purpose Input/Output (GPIO)
Bridge Status
Generic Device Status

## Slide 197: General Pupose Input/Output (GPIO): Status
Bridge status is monitored and sent to 511 via C2C
If configured as manual status, status can be directly change by the operator
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 198: General Purpose Input/Output (GPIO)
Configuration

## Slide 199: General Pupose Input/Output (GPIO): Device
New Bridges can be configured to have a manual status update or set to monitor a specific part of an XML datafeed.
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 200: General Pupose Input/Output (GPIO): Device Group
Logical devices can be grouped for ease in monitoring
Bridges can be the only item in a group
Device status is tied to the GROUP, not the device.
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 201: General Purpose Input/Output (GPIO): Icons
Icons for each status type can be configured per installations.
A default set of icons is provided
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 202: General Pupose Input/Output (GPIO): DMS Message Actions
Users can configure a message and the signs to pose the message based on the change of a GPIO group to a particular status
Messages are removed when the device changes status again
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 203: Part 5: Event Management

## Slide 204: Event Management

## Slide 205: EM: Purpose
Purpose of Event Management
Tracks event status and location
Assists in agency coordination
Coordinate devices and messages on DMS, HAR, 511, etc.
Tracks timestamps of what happened when
Designed to maximize operator’s performance so events can be handled as quickly as possible
Notes: Some examples of the various objectives that went into the design of SunGuide’s EM subsystem and GUI

## Slide 206: EM: Event List
Sort by Clicking Column Headers
Events Grouped
Notes: Can filter or search for events from list.
If operator logs off SunGuide and owns events, the events should be released.

## Slide 207: Event Management: Event List Settings
From the Event List dialog, Select Change Settings
Configure the color of the rows that are owned by the user (or turn the feature off)
Configure the warning color for a row with an active response plane that hasn’t’ been updated
Configure the number of rows each event list is displayed on in the Event List.
Notes: Response plans will be discussed in detail in the next section

## Slide 208: EM: Create New Event
Add basic initial information
Notes: Can filter or search for events from list.
If operator logs off SunGuide and owns events, the events should be released.

## Slide 209: Event Management: Create Planned Events
To create a planned event, select Event Management >> Add New Planned Event.
End time is Optional
Set Lane Blockage for the planned event as well.
Once created, Response Plans can be added (but not activated)
Notes: Response plans will be discussed in detail in the next section

## Slide 210: Event Management: Planned Events
Reminder notifications will pop up at the configured time to remind the operator about the start of the event
Numerous options for handling the planned event are available
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 211: EM: Open/Edit Events
Open/Edit an Event
  By clicking on the event from the Event List
  By clicking on the icon on the Map
Organized by Categories
  Administrative Details
  Impact on Roadways
  Reporting & Dispatch
  Event Details
  Comments
  Event History
Also lists timestamps when agencies were contacted, on scene, and departed
Unique event ID and location information
Notes: May be a good idea to define severity levels of incidents:
Unknown – Set if unknown event type
Minor – Default level or lane, ramp, or shoulder blockage or less than 30 minutes
Moderate - Lane, ramp, or shoulder blockage between 30 minutes and 2 hours
Major – All lanes blocked or all ramp lanes blocked or any lane blockage for more than 2 hours

## Slide 212: EM: Notified, On Scene, Departed Times
Notified, On Scene, and Departed times listed along right side of Event window
Automatically filled depending on operator actions
  For example, if reported by Road Ranger, then Road Ranger “Notified” and “On Scene” fields are automatically filled
Timestamps should chronologically occur from left to right
  Notified, then On Scene, and finally Departed
Timestamps can be manually set by clicking in empty boxes
Notes: To save a time, click in the box. The timestamp will appear blue until the “Save” button is pressed.
If multiple responders of the same responder type arrives (for example, if multiple FHP troopers arrive on scene), save the timestamp for the first responder, then save the timestamp of the next responder in the same box (overwriting the first timestamp). The GUI will only display the last timestamp saved, but SunGuide will archive all timestamps saved.

## Slide 213: EM: Ribbon Options
Save Changes
Obtain/Release Ownership
  Operator who created/last modified event has ownership
  Must “Obtain Ownership” in order to modify event
  Event is read-only if you do not “own” it
Clone Event
  Copies all details from an event into a newly created event with a new event ID
Manage a RISC associated to the event
Manage the planning of an event
Response Plan Generation/Edit/Termination
Locate on Map
Find the Nearest CCTV to the event
Generate Chronology Report
Expand/Collapse all of the section headers for the event
Notes: Operator is the operator who currently owns the event. An operator must own the event in order to edit it.
To obtain ownership, simply click the “Obtain Ownership” button.
When event is initially created, the status can only be set to Active or Unconfirmed.

## Slide 214: EM: Administrative Details
Operator
  Operator ID of who “owns” event
Date/Time Added and Status Last Updated
Status
  Unconfirmed – Event was reported but not confirmed
  Active – Event was reported and confirmed
  False Alarm – Event was reported, never confirmed or event was resolved before action was taken
  Void – Event was created mistakenly or event was already created
  Unresolved – Event was reported, confirmed, but there is nothing else operator can do. For example: Abandoned vehicle
  Closed – Issue resolved
Notes: Operator is the operator who currently owns the event. An operator must own the event in order to edit it.
To obtain ownership, simply click the “Obtain Ownership” button.
When event is initially created, the status can only be set to Active or Unconfirmed.

## Slide 215: EM: Administrative Details
Contacts (Optional)
  Add people/contacts who the operator coordinated with through the life of the event
  Contacting Agencies are pre-configured within SunGuide
    Operators cannot add/modify agencies
    Select “Other” for Agency if not listed
  Contact name and phone number recorded by operator
Notes: Operator is the operator who currently owns the event. An operator must own the event in order to edit it.
To obtain ownership, simply click the “Obtain Ownership” button.
When event is initially created, the status can only be set to Active or Unconfirmed.

## Slide 216: EM: Impact on Roadways
Event Location / Congestion
Lane Blockage / DMS Assignment
Anticipated Clearance Time
  Estimated Number of Minutes of when event may be cleared
  Typically only used for construction / planned events
FL-ATIS Incident Severity
  Auto-selected by SunGuide based on percentage of lanes blocked
  Operator must confirm severity and save event
  Operator can change severity if desired
Notes: To edit Event Location or Lane Blockage, click on hyperlinks.

## Slide 217: EM: Event Location
To add Congestion information, select the “Congestion” checkbox
Can be defined per approach
Congestion is defined as a road segment, instead of a single point
  Must define a start and end point
  Same fields used to define the start/end locations (county, road, direction, reference point, and relationship to exit)
Congestion Checkbox
Congestion Start/End
Notes: Select the event location FIRST, then check the “Congestion” button. The Congestion is the event location, the Congestion end is the upstream location; i.e. drivers will reach the Congestion end before reaching the Congestion start.

## Slide 218: EM: Lane Blockage
View Road Configuration and Designate which lanes / shoulders / ramps are blocked
Can be defined per approach
Lane Configuration automatically provided
  Can be changed using Insert Lane / Remove Lane
  Missing or incorrect lane configuration should be reported to SunGuide Administrator
Notes: Changing the lane configuration here only saves it for this event, it doesn’t change the lane configuration permanently.

## Slide 219: EM: Event Lane Configuration
Lane Numbering (1 to N lanes)
  Lane 1: Left side, nearest median (yellow stripe)
  Lane N: Right side, furthest from median (white stripe)
  Lane order does not change based on event direction
Lane Blockage
  Lane Attributes can be changes by left click
    M – Mainline
    HOV – High Occupancy Vehicle lane
    HOT – High Occupancy Toll lane
    On – On ramp
    Off – Off Ramp
    Sh – Shoulder
    G - Gore
  Change Lane Status
    Green Arrow – lane open
    Red X – lane blocked
    Question Mark – unknown status

## Slide 220: EM: Reporting & Dispatch
One or more Road Ranger (RR) Vehicles Dispatch
  Select RR from list
  Set Status: Patrolling, Arrived, Service, Departed
Timestamp buttons enabled in the order that they can be performed
  RR Dispatched
  RR Arrived
  Set RR Activity
    Gas, Water, Tire, Could not Assist, etc…
  RR Departed
If RR Tablet is used, fields are automatically filled in when RR driver makes selections on RR Tablet
  Operator must still “Dispatch” RR
Can add Procedure Errors if RR makes errors
  Failed to operate arrow board, etc.
Notes: Demonstrate the following…
Dispatching road rangers requires operators to select the vehicle and then click the “Dispatch” button.
If road ranger was incorrectly dispatched, click “Cancel” and then add a comment to request supervisor to audit event
Once “Dispatch” is pressed, “Arrive” button is visible.
If the road ranger tablet is used, the road ranger takes over from here. Otherwise…
Click “Arrive” when road range has arrived
Then assign activities by selecting an activity from the activities list and clicking “Add”
Additional activities can be added by selecting another activity and clicking “Add”
Once at least one activity has been added and the road ranger has departed, click the “Depart” button

## Slide 221: EM: Event Details
  Event Icon for Incident events depends on severity of event
    Event severity automatically selected based on lane blockage, injuries, event status
    Level 1: least severe
    Level 2: moderate
    Level 3: most severe
Notes: Specifying the CCTV is very helpful when managing multiple events at the same time; allows operators to go back to the event and reminds them what camera was near the event. Especially useful for abandon vehicles to check if the vehicle is still there hours later.
Clone events: Creates a new event at the same location and with the same event type as the original event. The cloned event will automatically “link” back to the original event by setting the “Primary Event” field.

## Slide 222: EM: Event Details
Only ONE event type per event
If multiple types apply, multiple event reports should be created
Notes: Specifying the CCTV is very helpful when managing multiple events at the same time; allows operators to go back to the event and reminds them what camera was near the event. Especially useful for abandon vehicles to check if the vehicle is still there hours later.
Clone events: Creates a new event at the same location and with the same event type as the original event. The cloned event will automatically “link” back to the original event by setting the “Primary Event” field.

## Slide 223: EM: Event Details
Event Attributes can be added or deleted by the user to represent trackable conditions from the event
These may later be used to report on particular types of events
Notes: Specifying the CCTV is very helpful when managing multiple events at the same time; allows operators to go back to the event and reminds them what camera was near the event. Especially useful for abandon vehicles to check if the vehicle is still there hours later.
Clone events: Creates a new event at the same location and with the same event type as the original event. The cloned event will automatically “link” back to the original event by setting the “Primary Event” field.

## Slide 224: EM: Event Details: Vehicles Involved
Can add / modify / delete details about one or more vehicle involved
Vehicle color, make, and model configurable in SunGuide
  If a common vehicle is not listed, SunGuide Administrator should be notified
Vehicle Tag and State
  If a vehicle with the same tag number was previously associated with an event, a link appears in the “Match” column indicating how many times vehicle is recorded
  Match links will open a list of previously entered events associated with tag
  Match intended to identify if a vehicle is abusing RR service such as repeatedly running out of gas
Notes: Vehicles can be added as long as the operator knows the vehicle color, other fields could remain unselected if unknown.
If road ranger tablet is used, road ranger will have the ability to add/modify this information.
Vehicle Matches: SunGuide will search its database for any other events with the same “Tag” and provide a list of other events to the operator. Allows operator to find drivers who are abusing road ranger service.

## Slide 225: EM: Event Details: Vehicles Involved
Vehicle Make/Model is configured within SunGuide
  Additional Make/Models may need to be added/modified over time
Notes: Vehicles can be added as long as the operator knows the vehicle color, other fields could remain unselected if unknown.
If road ranger tablet is used, road ranger will have the ability to add/modify this information.
Vehicle Matches: SunGuide will search its database for any other events with the same “Tag” and provide a list of other events to the operator. Allows operator to find drivers who are abusing road ranger service.

## Slide 226: EM: Event Details: Primary / Secondary Events and Injuries
Primary / Secondary Events
  If event is a Secondary Event, can associate a Primary Event
  Likewise, if event is a Primary Event, can associate a Secondary Event
  “Go to” buttons will open associated events in separate window
Specify injuries from configured list, if any
  If common injuries not in list, SunGuide Administrator should be notified
Notes: Link to primary set if current event is a secondary event.
Link to secondary set if current event is the primary event.

## Slide 227: EM: Event Details: Weather Conditions
Road Surface, Weather, Lighting
Default values are configurable, but do not vary based on time of day
  Most likely “Daylight” will be the default, so events entered at night need to be changed to Dark / Dusk / Dawn
Additional weather conditions cannot be added
  Use “All Other” or “Unknown” if selection does not describe conditions

## Slide 228: EM: Event Details: SAE Description
Based on Event Type, Vehicles Involved, Weather conditions, and lane blockage, SunGuide selects a SAE code / codes to send the 511 (FL ATIS) system
The interpretation of the SAE code / codes are what the 511 (FL ATIS) system reports to the public, in conjunction with EM Location information
The SAE Description field shows a textual interpretation of the codes that SunGuide selected based on operator selections
SAE Description should be similar to what the 511 (FL ATIS) system should report
Notes: SAE codes used to communicate event information to FL ATIS. This description should roughly match what is reported on FL ATIS.

## Slide 229: EM: Event Details: SAE Codes
Crash Involving Hazardous Materials:
  Select “Crash” from the event type drop-down.
  Check the “Hazardous Materials” box to indicate that hazardous materials are involved in the accident.
Multi Vehicle Crash:
  Select “Crash” from the event type drop-down.
  Add a minimum of two vehicles the list of involved vehicles.
Overturned Tractor/Trailer:
  Add an involved vehicle of vehicle type “Tractor/Trailer”.
  Check the roll-over box.
Crash Involving Tractor Trailer:
  Select “Crash” from the event type drop-down.
  Select a maximum of one vehicle to add to the involved vehicle list
  and ensure that the vehicle type is of “Tractor/Trailer”.
Crash Involving Bus:
  Select “Crash” from the event type drop-down.
  Select a maximum of one vehicle to add to the involved vehicle list
  and ensure that the vehicle type is of “Bus”.
Crash Involving Truck:
  Select “Crash” from the event type drop-down.
  Select a maximum of one vehicle to add to the involved vehicle list
  and ensure that the vehicle make contains the word “Truck”.
Notes: Following slides are for the operator’s reference.

## Slide 230: EM: Event Details: SAE Codes
Crash:
  Select “Crash” from the event type drop-down.
  Note: Involvement of a Tractor/Trailer, Bus, or Truck will cause one of the other accident types to be selected.
Emergency Road Construction:
  Select “Road Work - Emergency” from the event type drop-down.
Disabled Tractor Trailer:
  Select “Disabled Vehicle” from the event type drop-down.
  Select a vehicle to add to the involved vehicle list
  and ensure that the vehicle type is of “Tractor/Trailer”.
Disabled Bus:
  Select “Disabled Vehicle” from the event type drop-down.
  Select a vehicle to add to the involved vehicle list
  and ensure that the vehicle type is of “Bus”.
Disabled Truck:
  Select “Disabled Vehicle” from the event type drop-down.
  Select a maximum of one vehicle to add to the involved vehicle list
  and ensure that the vehicle make contains the word “Truck”.
Disabled Vehicle:
  Select “Disabled Vehicle” from the event type drop-down.
  Note: Involvement of a Tractor/Trailer, Bus, or Truck will cause one of the other disabled vehicle types to be selected.
Vehicle On Fire:
  Select “Vehicle Fire” from the event type drop-down.

## Slide 231: EM: Event Details: SAE Codes
Abandoned Vehicle:
  Select “Abandoned Vehicle” from the event type drop-down.
Planned Construction:
  Select “Road Work - Scheduled” from the event type drop-down.
Object On Roadway:
  Select “Debris on Roadway” from the event type drop-down.
Traffic Congestion:
  Select “Congestion” from the event type drop-down.
Bridge Maintenance Operations:
  Select “Bridge Work” from the event type drop-down.
Emergency Vehicles:
  Select “Emergency Vehicles” from the event type drop-down.
Off Ramp Backup:
  Select “Off Ramp Backup” from the event type drop-down.
Police Activity:
  Select “Police Activity” from the event type drop-down.
Interagency Coordination:
  Select “Interagency Coordination” from the event type drop-down.
Special Event:
  Select “Special Event” from the event type drop-down.
Incident: (Default event type)
  Select “Other” from the event type drop-down.

## Slide 232: EM: Event Details: Comments and Event History
Free text comments can be added by operator / supervisor to record notes specific to event
  Typically only used for unusual or abnormal situations or account for why certain operator / RR actions could not be performed
  Example 1: Lane blockage events should result in placing a message on a DMS. If the operator is reporting the event as the event clears, then a note can be added: “Event cleared before DMS message could be placed.
  Example 2: If a RR attempts to help the driver of a broken down vehicle and the driver refuses help, the following note can be added: “Driver refuses RR help”
Event History
  Lists every update / action / comment added or modified
  When read in order, tells the “story” of the event
Notes: The more the notes the better. If unsure of how to handle a situation, make a note or multiple notes.
Notes should added if event needs to be audited; if operator makes an error that would effect the performance measures, event should be audited.

## Slide 233: EM: Executive Notifications
Based on criteria set by the Central Office, notifications are automatically generated when certain conditions occur
Notifications for an email template are sent directly to the operators who owns the event
Users are able to format the email and add any additional information
Changes and new comments are highlighted
Comments can be included or excluded
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 234: Event Management
Configuration

## Slide 235: Event Management: Configuration
Direction Specific
One approach allowed per reference offset (at, before, beyond, rampTo, rampFrom)
Multiple approaches required for intersections (at intersection of)
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 236: Event Management: Configuration
Each can be used for multiple EM Locations
Notes: Response plans will be discussed in detail in the next section

## Slide 237: Event Management: Configuration
Recommend using the most common name if road spans multiple counties / regions
“Primary Roadway” can be used to signify the most common name, while allowing you to change the name of the road in certain areas
Notes: Response plans will be discussed in detail in the next section

## Slide 238: Event Management: Configuration
Notes: Response plans will be discussed in detail in the next section

## Slide 239: Event Management: Configuration
Lane types are fairly standard
Lane mapping should handle all possible lane configurations at locations
One lane mapping per permutation
Notes: Response plans will be discussed in detail in the next section

## Slide 240: Event Management: Configuration
A Guided Location Configuration is available under Configuration >> Event Management >> Locations >> Guided Location Configuration.
Guides users through each part of a location configuration
If configuration items are not available, the dialog links to each configuration dialog need to add the values.
SunGuide Operator Training, R8.0
Notes: Response plans will be discussed in detail in the next section

## Slide 241: Event Management: Configuration
Cannot be modified
Directly tied to performance measures
Changes require CMB approval
Reminder Threshold – The amount of time before the user should be notified of an event with no update and an active response plan
Priority Start/End – ranges a DMS message priority should be in for those event types
Notes: Response plans will be discussed in detail in the next section

## Slide 242: Event Management: Configuration
Both fairly standard, but can be modified if needed
Notes: Response plans will be discussed in detail in the next section

## Slide 243: Event Management: Configuration
Both fairly standard, but can be modified if needed
Notes: Response plans will be discussed in detail in the next section

## Slide 244: Event Management: Configuration
Used for Responders list
Responder type checkboxes are important for correct categorization
Contacts are imported from CNA and can be used with multiple agencies.
Notes: Response plans will be discussed in detail in the next section

## Slide 245: Event Management: Configuration
Used for linking DMS together so the correct DMS are suggested to operators within response plans
Allows to link DMS on different roadways and different directions
Should be linked based on how people normally travel
Notes: Response plans will be discussed in detail in the next section

## Slide 246: Event Management: Configuration
Used for event management coordination
Notes: Response plans will be discussed in detail in the next section

## Slide 247: Event Management: Configuration
Used for vehicles involved
FDOT CO provides default listing
Vehicle types cannot be modified – requires CMB approval
Notes: Response plans will be discussed in detail in the next section

## Slide 248: Event Management: Configuration
Fairly standardized
Procedural errors apply to RR management
Weather can only modify default conditions
Notes: Response plans will be discussed in detail in the next section

## Slide 249: Contact Notification Application (CNA)
Configuration

## Slide 250: CNA: Configuration
Users can add/modify/delete contacts in the system
Users can choose “New Delivery Method” to add ways to send a message to the user, but its only needed for the types of ways in which the contact would receive the message
Notes: Response plans will be discussed in detail in the next section

## Slide 251: CNA: Configuration
Users can add/modify/delete contact groups in the system
Groups can be made of contacts or other contact groups.
Notes: Response plans will be discussed in detail in the next section

## Slide 252: CNA: Configuration
Areas can be defined on the map
Contacts (or contact groups) added to the area for easy access at a known location
Notes: Response plans will be discussed in detail in the next section

## Slide 253: Response Plans

## Slide 254: EM: Response Plan Selecting a Response Plan
After clicking on “Save, Get Response”, the window above appears
Operator can modify the search distance, from the event location to the upstream DMS
  Type in “HAR radius” and/or “DMS radius” and click “Get New Suggestion”
Operator can view other plans
Review the proposed email message, DMS messages, & HAR messages
Click “Accept” once a Response Plan is determined
Modify search distance
View other plans
Get New Suggestion
Set as Response
Email to be sent
DMS Messages
HAR Messages
Notes: Review the Email, DMS, HAR, etc to ensure all desired dissemination outlets are listed.
SunGuide will pick DMS/HAR upstream of event of x number of miles. The x depends on the event severity, however, an operator can increase/decrease this range by changing the modify search distance and clicking “Get New Suggestion”

## Slide 255: EM: Response Plan Activate / Terminate Response Plan
After clicking on “Accept”, the window above appears
Click “Edit Item” or “Remove Item” to modify or remove email recipients, DMS, or HAR if needed/desired
“Activate Plan” will initiate Response Plan
  Upon activation, SunGuide will send emails and DMS messages
“Terminate Plan” will remove messages from DMS
Activate / Terminate Plan
Modify Email Recipients / DMS / HAR
Remove Email / DMS / HAR / 511
Notes: DMS/HAR/FL ATIS/Email can be individually removed or added or modified here.
Messages are not sent until “Activate Plan” is selected.
“Terminate Plan” will remove the DMS messages from their respective MAS queues, send out a “cleared” email, remove the HAR message, and remove the event from FL ATIS.

## Slide 256: EM: Response Plan Adding Email Recipients, DMS, and HAR
Click “Add Item” to add DMS or HAR device
  Operator will be prompted with a list of DMS/HAR devices to select
  Local or Remote/C2C DMS can be added to a response plan
Click “Add Item” to add email recipients
  Operator will be prompted with Email selection window
Click “Add Item” to add the 511 entry
  If 511 entry is in the response list when “Activate Plan” is selected, then event will be pushed to the 511 (FL ATIS) system
  Can add 511 entry if it was previously removed
Add Email Recipients / DMS / HAR / 511

## Slide 257: EM: Response Plan DMS Groups: Editing Multiple DMS
Hold Ctrl and left click all DMS that will be edited
Click the “Edit Item” button and the Message Editor Window appears
Modify the message in the Message Editor Window
Click “Save”, then “Activate Plan”
DMS Group
Notes: Selecting “group” allows editing multiple DMS at the same time.
Alternatively, you can select the first DMS in a group, hold shift, and select the last to select all DMS in between the two.

## Slide 258: EM: Response Plan Rule of Thumb #1
To remove a response plan message from the DMS message queue
  Preferred method would be to open response plan, remove selected DMS, and re-issue response plan
  Alternatively, open MAS queue for selected DMS and blank the entire queue

## Slide 259: EM: Response Plan Rule of Thumb #2
If the 511 system (FL ATIS) is not available or is down when a response plan was activated, the associated event(s) will have to be republished once the 511 system is back up
Notes: May be required even if FL ATIS is up and running. All FL ATIS updates should be verified.

## Slide 260: EM: Response Plan Rule of Thumb #3
If the 511 system (FL ATIS) is not available or is down when a response plan was terminated, the associated event(s) will have to be removed once the 511 system is back up
Notes: May be required even if FL ATIS is up and running. All FL ATIS updates should be verified.

## Slide 261: EM: Response Plan Additional Note
Un-merged Upon Termination
If a response plan DMS message is merged with another message and the response plan is terminated, the other message will be "unmerged" and will resume its normal location in the queue based on its priority after the response plan message is terminated.

## Slide 262: EM: Response Plan Additional Features
Click the “Suggestions” tab to go back to the Suggested Response Plan view
Click “Load Predefined” to load a new response plan created in the admin editor
Right click a device and select “Find on Map” from the context menu to highlight in red the device icon on the map
Add Predefined Plan
View Suggestions

## Slide 263: Rapid Incident Scene Clearance (RISC) Activations

## Slide 264: EM: RISC Activation New Activation
When starting a new activation, the user should select who is requesting the RISC and what equipment will be needed.
Notes: Response plans will be discussed in detail in the next section

## Slide 265: EM: RISC Activation Notify Contractor
The user should then notify the contract as directed by the dialog and select the ribbon button indicating they have notified the contractor.
Notes: Response plans will be discussed in detail in the next section

## Slide 266: EM: RISC Activation Notify Contractor
By clicking the Contractor Responded button in the ribbon, the user can track the response of the contractor.
Activate – the contractor has responded and will take the RISC.
Unable to Respond – Contact was made with the contractor but they are not able to respond at this time. A comment on why may be entered.
  Selecting this will allow the user to see the next contractor to notify.
No Response – No contact was made and time has expired.
  Selecting this will allow the user to see the next contractor to notify.
Notes: Response plans will be discussed in detail in the next section

## Slide 267: EM: RISC Activation Equipment Tracking
Equipment is tracked with Arrived and Verified times.
Equipment used in the clearance can be marked as “Utilized”
Notes: Response plans will be discussed in detail in the next section

## Slide 268: RISC Activations
User should click the ribbon button when the Notice to Proceed is given, stopped, resumed, cancelled, or voided.
Timestamps for each event will be tracked and shown to the user.
When all lanes are clear, the All Lanes Cleared button should be selected to finish the RISC.
Notes: Response plans will be discussed in detail in the next section

## Slide 269: RISC Activations
A RISC specific chronology is generated for the RISC activation
Each action is logged with the action and operator that performed the action
Notes: Response plans will be discussed in detail in the next section

## Slide 270: Event Management Auditing

## Slide 271: EM Audit – Configuring Request Audit Comment Type
Adding a special “Audit Requested” comment type:
gives operators the ability to flag an event and specify the needed correction

## Slide 272: Finding Event IDs of Audit Requests
Use Adobe Reader’s search function to find “Audit Request” (top of window)
Note the event number and requested change (embedded in the chronology entry)
Use the Audit Function in EM to make the correction to the event ID (next slides)

## Slide 273: EM Auditing
Audit Types:
  Notifying Agency and Contact
  Event Status
  Event Type
  Event Location and Congestion
  Lane Blockage
  Vehicle Dispatch
  Responder Times
  Vehicles Involved

## Slide 274: EM Auditing Notifying Agency and Contact
Change an event’s notifying agency and contact
Cannot change timestamps

## Slide 275: EM Auditing Event Status
Change the status of the event
Change the timestamp of the event status record
  For example: If the event should have been closed 15 minutes prior to the event actually being closed

## Slide 276: EM Auditing Event Type
Change the type of the event and click Update Record
Typically, the timestamp should not be changed nor should New Records be created. There only needs to be one event type record in the event at the time of creation

## Slide 277: EM Auditing Event Location and Congestion
Select operator action from Record History
Change the event location
Change the congestion head and/or tail
Must change the event location first before you can change the head and tail

## Slide 278: EM Auditing Lane Blockage
Select operator action from Record History
Change the lane blockage and lane clearance
Note: Lane blockage and lane clearance are different actions
Lanes should be blocked and cleared at accurate timestamps

## Slide 279: EM Auditing Vehicle Dispatch
Change the timestamps of vehicle’s dispatched, arrived, departed, or cancelled
Activities can be added but there’s not a way to add new vehicles dispatched to the events
  New vehicles would need to be added by opening event, adding vehicle(s), and closing event

## Slide 280: EM Auditing Responder Times
Change the Notified, On Scene, and Departed timestamps of vehicles from other (non-TMC managed) agencies

## Slide 281: EM Auditing Vehicles Involved
Add, modify, and delete vehicles involved

## Slide 282: EM Auditing Comments
Add, modify, and delete comments

## Slide 283: EM Auditing Event Details
Details about the event, including event attributes can be added, modified, or deleted
Notes: Response plans will be discussed in detail in the next section

## Slide 284: Incident Detection Subsystem (IDS)

## Slide 285: Incident Detection Subsystem
SunGuide will prompt operators of possible new events detected from external systems, such as weather systems or Citilog, or FHP CAD
No events will be created/updated without operator intervention
Upon detection, an alert will be reported in the alert box / window
  Alerts listed on right side of Events List
  Alert window can be opened from Operator Map, left click -> System ->System Alerts

## Slide 286
Can filter on the source of the alert
Resolve, Approve, Dismiss
Find on Map
Alert provides all pertinent information that is available. For FHP Alerts, provides county, roadway, and cross street (if available)
Incident Detection Subsystem

## Slide 287
Alert handling window differs based on the type of alert
Incident Detection Subsystem

## Slide 288
Handing an FHP alarm
Lists all information reported from FHP and nearby events
Note that FHP alert locations should be confirmed
Incident Detection Subsystem

## Slide 289: FHP Alerts: Key FHP CAD Fields

## Slide 290
Inter-operator Action Request
  Update event
  Transfer ownership
  Reject change
Incident Detection Subsystem

## Slide 291: IDS
Configuration

## Slide 292
IDS Citilog camera configuration
IDS: Citilog Cameras

## Slide 293: IDS: Wrong Way Driving

## Slide 294: Wrong Way Driving: Concept
Traffic Detector detects wrong way driving event at detector location
  Typically placed at Off Ramps
SunGuide receives alert
Email and Operator Alerts are automatically generated
Operator should confirm event
  Create an event report and generate a response plan, or
  Dismiss with possible cause
SunGuide
EXIT
TMC Operator
Alert
Email
Detected Wrong Way Driver
Event/ Dismiss
DMS
511
Other Coordination

## Slide 295: Wrong Way Driving: Operator Map
Operator Map icons
  Green: Device reporting heartbeat
  Blue: Device has stopped reporting heartbeat
  Red: SunGuide cannot communicate with device and/or device has failed

## Slide 296: Wrong Way Driving: Device Status
Context Menu
  Incident Detection -> Wrong Way Devices…
  Right-click on device icon -> Device Status…
Wrong Way Device Status window

## Slide 297: Wrong Way Driving: Device Status
Wrong Way Device Status
  Set Op Status
  Find on Map

## Slide 298: Wrong Way Driving: Configuration
Device Configuration
  Add, delete, find, and place on map
Can be placed on map so icon does not overlap existing icons

## Slide 299: Wrong Way Driving: Alerts
Alerts appear in alert box and popup window
Email alert sent to configured list of people

## Slide 300: Wrong Way Driving: Alerts
All popup alerts need to be handled by an operator
  Standard event report can be created, or
  Alert can be dismissed
New Event Type
New DMS / Email Message for RPG

## Slide 301: 511 Floodgates

## Slide 302: 511 Floodgates: Status
From the green selection bar, select “Floodgate Status” or from “Center-to-Center” and then “Floodgate Messages” from the Context menu to list all active 511 floodgate messages
Floodgates listed encompasses all floodgates in the FL ATIS system (accumulated from all districts)
Upon selecting any of the Floodgates, the Floodgate Main entry window will open for the selected Floodgate
Note: Coordinate with district who posted the floodgate prior to updating
Notes: This lists all floodgates in the FL ATIS system, regardless of the district.

## Slide 303: 511 Floodgates: Entry
Operator selects Floodgate level, corresponding to the 511 menu level that will play back the floodgate
Up to four floodgates can be recorded per language (English and Spanish) at a single level
Both English and Spanish voice and banner messages must be posted
Notes: When creating a floodgate, go from the top of this window, downward.
First select the Floodgate level; i.e. where the floodgate will be played on the 511 system.
Then select the floodgate number. The number is the order in which the floodgates at the same Floodgate level will be reported.
Then select the language; English or Spanish.

## Slide 304: 511 Floodgates: Levels
Statewide
  IVR: Played when anyone dials into IVR when there is an active statewide floodgate
  IVR: Played immediately following the intro message
  Web: Displays at top of window regardless of what region is selected

## Slide 305: 511 Floodgates: Levels
Regional Floodgate
  IVR: Played when someone dials into the IVR when there is an active regional floodgate and they respond affirmatively when asked if they would like to hear the regional floodgate
  IVR: The message is played immediately following the intro message and any active statewide floodgates
  Web: Display at the top of the window when the associated region is selected

## Slide 306: 511 Floodgates: Levels
County Floodgate
  IVR: Played when someone requests a county from the main menu and there is an active county level floodgate for that county or someone who requests traffic and then specifies a county at the “Which City County or Highway” menu
  IVR: A county floodgate will not be played for anyone who requests a highway at the main menu or at the “Which City County or Highway” menu
  Web: Display at the top of the window when the associated region is selected

## Slide 307: 511 Floodgates: Levels
Roadway Floodgate
  IVR: Played when someone requests a roadway from the main menu and there is an active roadway level floodgate for that roadway or someone who requests traffic and then specifies a roadway at the “Which City County or Highway” menu
  IVR: A roadway floodgate will not be played for anyone who requests a county at the main menu or at the “Which City County or Highway” menu
  Web: Displays at top of window regardless of what region is selected

## Slide 308: 511 Floodgates: Levels
Roadway within a County Floodgate
  IVR: Played when someone first requests a County at either the main menu or at the “Which City County or Highway” menu, and then requests a roadway from the list of roadways presented by the IVR
  IVR: If there are no incidents within the County or no incidents for the roadway for which there is an active floodgate, then the caller will not have an option to chose that roadway and the floodgate will not be heard.
  Web: Display at the top of the window when the associated region is selected

## Slide 309: 511 Floodgates: Store Floodgate Dialog
Click Store Floodgate from Main Page to launch dialog
Select desired folder or subfolder
Provide a name to represent the floodgate
Click Store
All floodgate information is saved for later use via Load Floodgate
Notes: District 2 has offered to handle Spanish translations for other districts without Spanish-speaking/writing operators.
Each workstation should be set up to accommodate this.

## Slide 310: 511 Floodgates: Store Floodgate Dialog
Retrieve stored Floodgate that was previously saved
Notes: District 2 has offered to handle Spanish translations for other districts without Spanish-speaking/writing operators.
Each workstation should be set up to accommodate this.

## Slide 311: Event Management, Incident Detection, 511 Floodgates
Hands on
30 Minutes

## Slide 312: Road Ranger Management (AVI/RR)

## Slide 313: AVI/RR
AVI/RR (Advanced Vehicle Identification / Road Ranger)
  Allows operator to track RR location and availability status
    Real-time and archived
  Alerts operators if RR leaves patrolling area and stop alerts
  Facilitates communication with Road Rangers
  Allows dispatching and event updating

## Slide 314: AVI/RR

## Slide 315: AVI/RR Alerts
Geofence and stop alerts display a red blinking circle around the RR vehicle which triggered the violation
Geofence alerts are archived in the database and can be viewed using the Geofence Report

## Slide 316: AVI/RR
Vehicle Location Replay
  View vehicle locations over selected time

## Slide 317: AVI/RR
Configuration

## Slide 318: AVI/RR Configuration
Configure Road Ranger operators and radios

## Slide 319: AVI/RR Configuration
Agency and Vehicle configuration
  RR can use one of several devices

## Slide 320: AVI/RR Configuration
Customize statuses to better manage RR

## Slide 321: AVI/RR Configuration
Specify where a RR can patrol
  Offset is in feet

## Slide 322: AVI/RR Configuration
Vehicle status relates RR operators with beats and status

## Slide 323: AVI/RR Configuration
Beat configuration uses Geofence

## Slide 324: Smart Phone Application for Road Rangers (SPARR)

## Slide 325: SPARR: Overall Concept
Purpose of SPARR is to allow Road Rangers to view and/or edit traffic events to/from SunGuide using a Smart Phone application
Internet
SunGuide
511
DMS
Email/Texts
Road Ranger with SPARR

## Slide 326: SPARR: Configuration
From the context menu button on the Smart Phone, select “Configure”
Set publically accessible URL of SunGuide SPARR web service
Server username/password
Configuration password specified in config.xml file

## Slide 327: SPARR: Configuration
Login using SunGuide credentials
Set vehicle, radio, and route to start patrol

## Slide 328: SPARR: Configuration
Once patrol has started, events will be displayed if RTMC operator has dispatched to selected RR
Can create new events
Can change patrolling status

## Slide 329: SPARR: Configuration
When creating events, set event type and location
After event is created, set “Arrive” (if RTMC dispatched) or “Depart”
Add Services and Vehicles
Lane blockage must be set by the RTMC operator

## Slide 330: SPARR: Configuration
Services can only be added, not removed
Vehicle information can include any of the fields shown

## Slide 331: Road Ranger Management
Hands on
30 Minutes

## Slide 332: Part 6: Reporting

## Slide 333: Reporting Subsystem

## Slide 334: Reporting Subsystem
SunGuide has a wide variety of report templates that can export reports with archived subsystem data
These templates are initially grouped by similar type or functionality but are configurable

## Slide 335: Reporting Subsystem
Organize Reports into Report Groups
Add Reports by importing reporting template
  Templates can be requested from FDOT CO
  Brian Ritchson

## Slide 336: RS: Reporting Subsystem
“Out of the Box” Report Groups
  Event Management: Event-related reports
  Performance Measures: Weekly, monthly, quarterly, and annual reports required for statewide performance measures
  Road Ranger: Road Ranger management-related reports
  AVL Report: Reports archived AVL locations
  TSS: Traffic flow report
  Device: Reports for various devices (DMS, TSS, CCTV, etc)
  Software System: SunGuide computer system report
Notes: If operator logs off SunGuide and owns events, the events should be released.

## Slide 337: Reporting Subsystem
Access the Reports page
  map -> right click -> Reporting -> Generate Reports
Select the desired Report

## Slide 338: Reporting Subsystem
Enter in the desired filter parameters
Generate the report by clicking the button of the desired format
Notes: For some Event Management reports, there are a series of filters that can be used to narrow the search
parameters. Reports may be filtered by event number or range, specific date or range, day of
week, specific time or range, location (county, road, direction, exit), event type, status, notifying
agency, worst lane blockage, vehicle type, injuries, duration, responding agency, DMS usage,
severity level, Road Ranger procedural error, or any combination thereof.

## Slide 339: Reporting Subsystem
Report Queue Options
  Cancel Report
  Download Report
  Email Report

## Slide 340: Reporting Subsystem
Configuration

## Slide 341: Reporting Subsystem
Create reporting templates with Crystal Reports (outside SunGuide)
Upload template here
Categorize reports

## Slide 342: Regional Integrated Transportation Information System (RITIS)

## Slide 343: What is RITIS?
A giant traffic information data warehouse
Provides numerous reporting tools
All FDOT districts are providing data to it as well as other states/agencies throughout the US

## Slide 344: Accessing RITIS
Internet accessible
Requires login
  https://www.ritis.org
Each district has been provided login credentials
  Contact FDOT CO for credentials

## Slide 345: RITIS: Map-based reporting
System has the ability to provide map-based traffic conditions, events, camera images, etc
FDOT currently only providing detector and event information

## Slide 346: RITIS: Tabular and Data Downloads
System as various reporting formats
Determines frequent congestion areas
Users can download or view data
Data updates about every 15 mins

## Slide 347: Reporting
Hands on
20 Minutes

## Slide 348: Part 7: Additional Traffic Management

## Slide 349: Managed Lanes

## Slide 350: Managed Lanes
What is the Managed Lanes Subsystem?
Allows the control of managed lanes DMS and gates
Relies on traffic operational procedures

## Slide 351: Managed Lanes: Action Lists
Allowable operator actions
Includes setting configured gate(s) and DMS(s) based on predefined action templates
Confirm actions via cameras

## Slide 352: Managed Lanes: Action Lists
Execute actions
  View Status
  Verify
  Override

## Slide 353: Managed Lanes: Controller Status
View lane controller status via map icons and status window

## Slide 354: Managed Lanes: Ramp Status
View ramp controller status via map icons and status window

## Slide 355: Managed Lanes
Configuration

## Slide 356: Managed Lanes: Configuration
Configure roads to be managed and define segments within each

## Slide 357: Managed Lanes: Configuration
Configure controllers and gates

## Slide 358: Managed Lanes: Configuration
Configure segments and their ramps
  Specify gates and controllers per ramp

## Slide 359: Managed Lanes: Configuration
Define Action Lists
  New Action DMS and Gate templates

## Slide 360: Managed Lanes: Configuration
Define Prerequisite Actions
  Should occur prior to actions

## Slide 361: Managed Lanes: Configuration
DMS Action
Gate Action
  Note only groups of gates can be selected

## Slide 362: Traffic Control Subsystem

## Slide 363: Traffic Control Subsystem
What is the Traffic Control Subsystem?
Designates routes
Allows enabling response plan timing plans
Plans based on severity:
  Default
  Low
  Medium
  High

## Slide 364: Traffic Control
Operator map icons indicate status of SunGuide communication with traffic signal controller
Note individual devices are not configured in SunGuide – only with a master control system

## Slide 365: Traffic Control
Lists Timing Plans and associated traffic signals
Operator selects and activates plan

## Slide 366: Traffic Control: Response Plans
When editing a response plan, routes and signal route can be selected

## Slide 367: Traffic Control
Configuration

## Slide 368: Traffic Control: Configuration
Define routes and specify timing plans from selected controllers

## Slide 369: Truck Parking Subsystem

## Slide 370: Truck Parking
What is the Truck Parking Subsystem?
Monitors available truck parking spaces
Captures parking alarms based on configured thresholds

## Slide 371: Truck Parking
Map icons indicate communication status
Facility status displays available spaces and alarm status
Links to DMS and camera

## Slide 372: Truck Parking
Operator can modify available spaces and set active

## Slide 373: TPS Diagnostic Status
Diagnostics and sensors can be retrieved from the sign
Status for each sensor is reported along with other sensor details
Image of the parking facility can be configured and sensors placed on the map to view positioning
Status only view. No user input in this dialog.
Notes: Response plans will be discussed in detail in the next section

## Slide 374: Truck Parking
Configuration

## Slide 375: Truck Parking: Configuration
Configure parking facilities and parking zones

## Slide 376: Truck Parking: Configuration
Add DMS(s)
Add Camera(s)

## Slide 377: Truck Parking: Configuration
If presence detectors used, configure link(s)

## Slide 378: Truck Parking: Configuration
If passage detectors used, configure link(s)

## Slide 379: Ramp Metering

## Slide 380: Ramp Metering
Ramping Metering uses a Ramp Meter Controller (RMC) at ramps to regulate the flow of traffic entering limited access roads (I-95) according to current traffic conditions
SunGuide can monitor these RMC’s and set the algorithm that the controller should use
If configured, SunGuide can set the signaling state (Red / Green) based on “Fuzzy” Logic configured within SunGuide

## Slide 381: Ramp Metering Device Status
SunGuide map reports Ramp Meter Controller devices, ramp lanes, mainline lanes as color-coded icons
Ramp Meter Controller
Ramp Lanes (Angled)
Mainline Lanes (Straight)

## Slide 382: Ramp Metering Device Status
List of devices, status, control

## Slide 383: Ramp Metering Device Status
Set Active / Out of Service
Refresh Status
Set Metering Mode:
  Fuzzy / Local: RMC is on and using Fuzzy / Local algorithm
  Off: RMC is not operating
Set Range:
  Min/Max Rates
Set Rate:
  Number of Allowable Vehicles
Download Parameters:
  Acquire logic parameters from controller
Reset:
  Controller, Loops, and/or Communications

## Slide 384: Ramp Metering Device Status
Set Range
Set Rate
Resetting

## Slide 385: Ramp Metering Device Status
Ramp Occupancy and Advanced Queue Occupancy
Metering Rate: The rate of traffic allowed to enter mainline
Red Violator: Vehicle count of red light violators
Ramp Queue
Advanced Queue

## Slide 386: Ramp Metering
Configuration

## Slide 387: Ramp Metering Configuration
Add / Delete / Edit Sites

## Slide 388: Ramp Metering Configuration
Controller Connectivity and Location
TSS Lane Configuration (TSS configured prior)

## Slide 389: Ramp Metering Configuration
Parameters and Rules Acquired from controller

## Slide 390: Ramp Metering
Hands on
30 Minutes

## Slide 391: Remote Command Application (RCA)

## Slide 392: Remote Command Application
Districts can use the RCA module to bring in data from different installations
Devices data was integrated into the existing dialogs
  Device commands to remote devices are done from the same dialogs as local devices
Local and remote events are available to the user.
  Events can be added, modified, and deleted in the remote system.
Notes: Response plans will be discussed in detail in the next section

## Slide 393: Remote Command Application
A Center ID column is available to filter to a specific district data
Local and Remote devices are included in the same log
Notes: Response plans will be discussed in detail in the next section

## Slide 394: Remote Command Application
Configuration

## Slide 395: Remote Command Application
Using the Ribbon button, a local certificate can be generated for the installation. This can be provided to other districts to securely connect to the system.
If a remote district has given a file, that file can be imported using the Upload Remote Certificate ribbon button.
Settings for username and port will need to be given from the remote district.
Notes: Response plans will be discussed in detail in the next section

## Slide 396: SunGuide Operator Training
Release 8.0
Please fill out training surveys before leaving